## Slide 1: Homework #4: Cache November 6th, 2019
Jae W. Lee (jaewlee@snu.ac.kr)
Computer Science and Engineering
Seoul National University
TA: Yunho Jin, Jeonghun Gong

## Slide 2
Goal of This Project
You will be asked to write a cache simulator
  Understand cache structure
  Implement cache policy

## Slide 3: Setup
You need Linux environment
Install valgrind tool for extracting memory traces
Download PA4.tar from eTL
linux> sudo apt-get install valgrind
linux> tar -xvf PA4.tar
linux> cd PA4
linux> make clean; make

## Slide 4: What You Need to Do
Your Task: Implement a cache simulator producing the same output as the reference simulator (=csim-ref)
Reference cache simulator can simulate a cache with
  Arbitrary cache size
  Arbitrary associativity
  LRU replacement policy
File to modify (and submit): csim.c

## Slide 5: Test your code: An Example

## Slide 6: Helper Programs
valgrind : generate trace files
valgrind output
            <[operation] address, size >
I: instruction load (no space before [operation])
L: data load
S: data store
M: data modify (store after load)
linux> valgrind --log-fd=1 --tool=lackey -v --trace-mem=yes ls -l > <filename.trace>

## Slide 7: Helper Programs
csim-ref: reference cache simulator program
  -h: optional help flag
  -v: optional verbose flag
  -s: # of set index bits(S = 2s number of sets)
  -E: number of lines per set (=associativity)
  -b: block bits (B = 2b bytes per block)
  -t: trace file
linux> ./csim-ref [-hv] -s <s> -E <E> -b <b> -t <trace file>

## Slide 8: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 9: Program rules
csim.c should run without failure
Should work for arbitrary s, E, b
Focus only on data cache
  ignore “I” operations in traces
  “I” operations start in the first column while others start in second (should help you parse trace files)
Call printSummary() in cachelab.c at the end of your main function
  printSummary(hit_count, miss_count, eviction_count);
All memory accesses are aligned properly
  Single memory access does not cross block boundary

## Slide 10: Submission
Compress your source code and write-up into a single zip file.
  Compress csim.c and your report.
  Filename should be [student_id].zip (example: 2019-12345.zip).
  Please submit it in ZIP format. Other formats are not accepted.
Submission deadline: By 2019. 11. 20 (Wed) 23:59 KST

## Slide 11: Grades
Writeup: 10%
Late Submission:
  Within next 24 hours: 10% deduction
  Within next 48 hours: 30% deduction
  Within next 72 hours: 50% deduction
  After next 72 hours: Submission not accepted